MOHAWK MODEL SYSTEM IA-10 SPECIFICATIONS

HEAVY DUTY TWIN POST VEHICLE LIFT

1.0   SCOPE

1.1		THIS SPECIFICATION SETS FORTH THE CUSTOMERS’ REQUIREMENTS FOR THE 	PURCHASE OF A HEAVY DUTY TWO-POST, FRAME CONTACT, ABOVE GROUND LIFT 	DESIGNED FOR LIFTING VEHICLES WEIGHING UP TO 10,000 LBS. THIS IS THE ONLY 	TYPE OF LIFT THAT WILL BE ACCEPTED.

1.1.1	PER ANSI STANDARD ANSI/ALI ALCTV; OVERLOADING SWING ARMS IS NOT RECOMMENDED.  AS A 10,000 LB. CAPACITY LIFT, MAXIMUM CAPACITY PER ARM EQUALS 2,500 LBS.  EXERCISE CAUTION AS SOME 8,000 LB. VEHICLES MAY WEIGH OVER 5,000 LBS. ON REAR AXLE.

1.1.2	ALL EQUIPMENT SHALL BE NEW AND UNUSED. THE MODEL BEING BID MUST BE THE MANUFACTURER’S CURRENT PRODUCTION MODEL. USED, RECONDITIONED, LEFT OVER OR DISCONTINUED MODELS WILL NOT BE ACCEPTED.

1.1.3	EQUIPMENT MUST COMPLY WITH ALL APPLICABLE FEDERAL, STATE, AND LOCAL REGULATIONS AND MEET OSHA, UL-201, NEC, AND THE ANSI/ALI ALCTV 2011 AUTOMOTIVE LIFT STANDARD. THIS IS THE ONE AND ONLY NATIONALLY RECOGNIZED SAFETY STANDARD FOR VEHICLE LIFTS.

1.1.4	EQUIPMENT MUST BE STRUCTURALLY AND SAFETY TESTED AND CERTIFIED TO THE ANSI/ALI ALCTV 2011 AUTOMOTIVE LIFT STANDARD, A COPY OF LISTING CERTIFICATION SHALL BE SUPPLIED AS PART OF THE ACCEPTANCE OF THE BID.

1.1.5	EQUIPMENT MUST BE SUPPLIED WITH ALL ANSI, ALI SAFETY BOOKLET, ANSI OPERATIONS, INSTALLATION, AND MAINTENANCE BOOKLETS, ANSI/ALI ALOIM-2008 STANDARD AND LIFTING POINT GUIDES.

1.1.6	EQUIPMENT MUST BE SUPPLIED WITH ALL ANSI, ALI SAFETY DECALS. DECALS MUST BE PERMANENTLY PLACED ON THE LIFT IN CLEAR VIEW FOR THE OPERATOR.

1.2	THE MANUFACTURER MUST BE A FIRM REGULARLY ENGAGED IN THE DESIGN AND MANUFACTURING OF THE TYPE OF EQUIPMENT SPECIFIED HEREIN FOR A MINIMUM OF 5 YEARS, MANUFACTURING TWO POST LIFTS.

1.2.1	EQUIPMENT BEING OFFERED MUST BE A MODEL THAT HAS BEEN IN PRODUCTION FOR A MINIMUM OF 5 YEARS. A USERS LIST MUST BE AVAILABLE AT THE BUYER’S REQUEST.

1.2.2	ON REQUEST, THE BUYER MUST RECEIVE A CURRENT USERS LIST FOR THE SPECIFIED STYLE AND LIFT CAPACITY.

1.3	ALL MATERIAL THICKNESS AND STRUCTURAL DIMENSIONS ARE MINIMUMS DIMENSIONAL TOLERANCES UNLESS NOTED AS FOLLOWS;  ( 0.25 INCHES FOR DIMENSIONS LESS THAN 10 INCHES;  ( 1.0 INCHES FOR DIMENSIONS FROM 10 INCHES TO 5 FEET INCLUSIVE; ( 1.5 INCHES FOR DIMENSIONS GREATER THAN 5 FEET.

2.0   LIFT

2.1	COMPLETE LIFT ASSEMBLY SHALL CONSIST OF AN ELECTRIC OVER HYDRAULIC LIFT UNIT, CONTROLS, ANY ACCESSORIES AS SPECIFIED HEREIN.

2.2	LIFTING CAPACITY WILL BE 10,000 LBS. MINIMUM.

2.3	LIFTING HEIGHT (STROKE) WILL BE 72” MINIMUM. THIS DIMENSION IS MEASURED FROM THE FLOOR TO UNDERNEATH THE SWING ARM WHEN THE LIFT IS AT FULL HEIGHT. MEASUREMENT TO THE TOP OF THE SWING ARM SHALL NOT BE ADDED TO THE VERTICAL TRAVEL TO ARRIVE AT LIFTING STROKE.

2.3.1	LIFTING HEIGHT WILL BE 75-1/2” MINIMUM. THIS MEASUREMENT IS MEASURED FROM 	THE FLOOR TO THE TOP OF THE LIFTING PAD WHEN THE LIFT IS AT FULL HEIGHT AND THE LIFTING PAD IS AT ITS LOWEST POSITION.

2.3.2	LIFTING HEIGHT WILL BE 78-1/2” WITH 3” TRUCK ADAPTER, 81-1/2” WITH 6” TRUCK 	ADAPTER AND 84-1/2” WHEN THE 3” AND 6” ADAPTERS ARE STACKED TO 9”.2.3.3	GRAVITY ACTIVATED LOCKS IN EACH COLUMN WORKING INDEPENDENTLY OF 	EACH OTHER SHALL START LOCKING AT A MINIMUM OF FIVE (5) INCHES OFF 	THE FLOOR. THE MECHANICAL LOCKS IN EACH COLUMN WILL ENGAGE 	EVERY THREE (3) INCHES THEREAFTER TO FULL LIFTING HEIGHT.

2.3.3.1	LOCK BODY WILL BE MADE OF 3/4” THICK A-36 GRADE STEEL MEASURING 4”X6”.

2.3.3.2	EACH INDIVIDUAL LOCKING DEVICE SHALL BE CAPABLE OF SUPPORTING THE 	ENTIRE RATED LOAD OF THE LIFTING LEG.

2.3.3.3	THE LOCKING MECHANISM SHALL BE MECHANICALLY OPERATED AND SHALL 	NORMALLY BE ENGAGING A LOCKED POSITION.

2.3.4	THE MECHANICAL LOCKS ARE RELEASED MANUALLY. THE MECHANICAL LOCKS 	WILL RE-ENGAGE AUTOMATICALLY EVERY TIME THE LIFT IS RAISED. THE 	MECHANICAL LOCKS SHALL ALLOW THE OPERATOR TO RELEASE THE LOCKS 	AND LOWER THE LIFT WITHOUT CONTINUING TO HOLD A LOCK RELEASE. AIR 	OPERATED LOCK RELEASE IS NOT ACCEPTABLE DUE TO RELIANCE ON 	COMPRESSED AIR SUPPLY.

2.4	LIFTING SPEED WILL BE 45 SECONDS MINIMUM FROM THE FLOOR TO FULL 	HEIGHT.

2.5	LIFTING COLUMN

2.5.1	EACH COLUMN WILL BE CONSTRUCTED OF 3/4-INCH #2434 FORKLIFT CHANNEL 	AND BE RIGIDLY SUPPORTED AND JOINED TOGETHER WITH 3/4-INCH STEEL PLATE 	USING 3 POINT FILLET WELDS. FORMED, TUBULAR, OR BENT COLUMNS ARE NOT 	ACCEPTABLE.2.5.2	EACH COLUMN WILL BE A MINIMUM OF 19” WIDE X 9” 	DEEP. THESE LARGER 	HEAVY DUTY COLUMNS GIVE BETTER, SAFER SUPPORT 	WHEN LIFTING HEAVIER, 	UNEVEN LOADS. SMALLER LIGHTER DUTY 	COLUMNS WILL NOT BE ACCEPTED.

2.5.3	EACH COLUMN WILL HAVE A BASE PLATE MADE FROM 3/4” THICK GRADE A-36 	STEEL PLATES, MINIMUM. THE BASE PLATE WILL BE 29-1/2” X 19”, MINIMUM. THIS 	LARGE BASE PLATE IS DESIGNED TO HAVE LESS THAN 50 PSI OF PRESSURE ON 	THE CONCRETE FLOOR WITH A FULL LOAD.

2.5.3.1	EACH LIFT BASE PLATE WILL BE SECURED TO THE SHOP FLOOR USING EIGHT (8) 	3/4" X 5” WEJ-IT BRAND ANCHOR BOLTS.

2.6	CARRIAGE ASSEMBLY

2.6.1	EACH COLUMN WILL HAVE A CARRIAGE CONSTRUCTED OF 3/4- INCH STEEL 	PLATES JOINED TO A 3/8-INCH BACKING PLATE BY 3 POINT FILLET WELDS, 	MINIMUM.

2.6.2	THE CARRIAGE ASSEMBLY WILL ROLL UP AND DOWN SMOOTHLY IN THE 	FORKLIFT MAST COLUMNS ON FOUR (4) 4 INCH DOUBLE SEALED SELF-	LUBRICATING STEEL BALL BEARING ROLLERS. PLASTIC OR NYLON TYPE SLIDE 	BLOCKS AND BUSHING TYPE ROLLERS ARE NOT ACCEPTABLE.

2.6.3	THE CARRIAGE ASSEMBLY SHALL NOT REQUIRE ANY MONTHLY CLEANING WITH 	SOLVENTS OR ANY LUBRICATION. ALL WEAR SURFACES SHALL BE COMPLETELY 	SEALED & SELF LUBRICATING WITH NO GREASE REQUIREMENTS.

2.6.4	THE CARRIAGE WILL ALSO INCLUDE (4) 2 INCH DOUBLE SEALED SELF 	LUBRICATING STEEL NEEDLE BEARING ROLLERS ACTING AS SIDE LOAD 	BEARINGS 	TO ELIMINATE THE STRESS OF UNEVENLY DISTRIBUTED LOADS. 	PLASTIC OR 	NYLON TYPE BEARINGS OR SLIDE BLOCKS ARE NOT ACCEPTABLE

2.6.5	THE CARRIAGE WILL BE LIFTED BY 1 3/4” WIDE #BL-646 LEAF CHAIN (MINIMUM), 	ROLLING OVER TWO (2) DOUBLE SEALED SELF-LUBRICATING CHAIN BEARINGS. 	SINGLE CHAIN BEARING AND BUSHING TYPE ROLLERS ARE NOT ACCEPTABLE.

2.6.6	CARRIAGES WILL SUPPORT THE SWING ARMS BY SANDWICHING THEM IN 	BETWEEN 2 PIECES OF 3/4 - INCH STEEL PLATE THAT IS JOINED TOGETHER BY 3 	POINT FILLET WELDS. THE SWING ARMS WILL BE HELD IN PLACE BY A 1- 3/8 INCH 	DIAMETER STEEL PIN WITH NYLON LOCK NUTS ON EACH SIDE. SWING ARMS THAT 	ARE NOT SUPPORTED BY A “TOP PLATE AND BOTTOM PLATE” ON THE CARRIAGE 	ARE NOT ACCEPTABLE DUE TO UNACCEPTABLE FLEX, WHICH PROMOTE 	PREMATURE WEAR.

2.7	LIFTING ARMS

2.7.1	MINIMUM ARM HEIGHT FROM FLOOR TO TOP OF LIFTING PAD IS 3 1/2”.

2.7.2	LIFTING ARMS WILL BE A CONSTRUCTED OF TWO PIECES OF GRADE A-500-B 	STRUCTURAL TUBING. THIS TUBING MUST HAVE A MINIMUM TENSILE STRENGTH 	OF 75,000 PSI AND MINIMUM YIELD STRENGTH OF 60,000 PSI.

2.7.3	THE FIRST PIECE CALLED “SWING ARM” WILL BE MADE OF 3” X 5” X 1/4” WALL 	THICKNESS. THE SECOND PIECE CALLED “SLIDER” WILL BE MADE FROM 2” X 4” X 	3/8” THICK WALL. SLIDER ENDS SHALL BE CAP WELDED CLOSED ON BOTH 	ENDS FOR ADDED STRENGTH.

2.7.4	LIFTING ARMS WILL ACCOMMODATE THE SMALLEST OF COMPACT CARS 	THROUGH LIGHT DUTY TRUCKS AND VANS WEIGHING UP TO 10,000 LBS.

2.7.5	LIFTING ARMS WILL HAVE A CLOSED REACH OF 35-3/4” AND AN OPEN REACH OF 	54-11/16”. ALL FOUR LIFTING ARMS WILL BE EQUAL IN LENGTH TO SAFELY 	SUPPORT FRONT WHEEL DRIVE VEHICLES AS WELL AS VEHICLES WITH DUAL 	REAR WHEELS, LIFT GATES, DUMP BODY AND UTILITY BODIES. ASYMMETRICAL 	LIFT ARMS ARE NOT ACCEPTABLE DUE TO UNACCEPTABLE FLEX OF LONGER 	REAR ARMS.

2.7.6	LIFTING ARMS WILL BE EQUIPPED WITH AUTOMATICALLY ENGAGING SWING 	ARM RESTRAINTS. MANUALLY OPERATED ARM RESTRAINTS ARE NOT 	ACCEPTABLE.

2.7.7 	SWING ARM RESTRAINTS WILL BE MADE FROM 1” DIAMETER HEAT TREATED 	ROCKWELL HARDNESS 50/55 GRADE 8 STEEL PINS THAT SLIDE THROUGH THE 	CARRIAGE AND ARE FORCED DOWNWARD BY A TENSIONING SPRING. THE 	TENSIONING SPRING FORCES THE PIN TO WEDGE AGAINST THE SWING ARM 	SECURING IT IN PLACE. THE SWING ARMS AUTOMATICALLY SECURE 	THEMSELVES WHEN THE LIFT IS RAISED AND RELEASE AUTOMATICALLY WHEN 	THE LIFT IS LOWERED ALL THE WAY DOWN.

2.7.7.1	ARM RESTRAINTS WILL BE OF AN INFINITE POSITION DESIGN CAUSING ARMS TO 	BE HELD IN PLACE AT EVERY POINT IN THEIR ROTATION.  GEARED TEETH TYPE 	ARM RESTRAINTS ARE NOT ACCEPTABLE DUE TO FINITE POSITION RESTRAINT 	LOCATIONS AND CHIPPED GEARS FOUND ON THIS DESIGN WHICH WHEN 	“CHIPPED” CAUSE ARMS TO NOT HOLD POSITION.

2.7.8	LIFTING PADS WILL BE MADE FROM 3-3/4” X 5-3/4” STEEL PLATE WITH STEEL 	CORRUGATED SURFACE FOR POSITIVE GRIPPING ON FLAT SURFACES OR LIFTING 	BY UNIBODY PINCH WELDS. RUBBER OR PLASTIC PADS ARE NOT ACCEPTABLE 	DUE TO WEAR AND DECREASED CO-EFFICIENT OF FRICTION AS RUBBER AND 	PLASTIC PADS GET OILY. WHILE NOT RECOMMENDED, WHEN INSISTED BY 	CUSTOMER, RUBBER TOPPED PADS ARE ALSO AVAILABLE AS AN OPTION AND 	SHALL BE ALI CERTIFIED.

2.7.9	LIFTING PADS MUST HAVE A 3-3/4” X 5-3/4” LIFTING SURFACE AT ALL TIMES 	INCLUDING WHEN TRUCK ADAPTERS ARE IN USE. SMALLER LIFTING SURFACES 	SUCH AS FLIP-UP PADS ARE NOT ACCEPTABLE.

2.8	LIFT DIMENSIONS

2.8.1	COLUMN HEIGHT 8’7” MAXIMUM

2.8.2	HYDRAULIC LINE HEIGHT SET AT TWELVE (12) FOOT STANDARD HEIGHT; 	ADJUSTABLE TO ACCOMMODATE ANY CEILING HEIGHT. LIFTS WITH 	OVERHEAD CABLE COVERS THAT REQUIRE AN ELECTRICAL SAFETY SHUT-OFF 	SWITCH ARE NOT ACCEPTABLE.

2.8.3	OPTIONAL IN FLOOR HYDRAULIC LINES ROUTED IN THE CONCRETE SLAB 	USING 	SEAMLESS STAINLESS STEEL HYDRAULIC LINES. THIS FEATURE LEAVES 	NO OVERHEAD LINES ALLOWING FOR TALLER VEHICLES TO BE LIFTED THE FULL 	6’ LIFTING HEIGHT AND OVERHEAD CRANES TO MOVE FREELY AROUND THE LIFT.

2.8.4	WIDTH BETWEEN COLUMNS WILL BE TEN (10) FOOT STANDARD, MINIMUM. WIDTH 	CAN BE ADJUSTABLE TO ACCOMMODATE WIDER VEHICLES OR NARROWED FOR 	TIGHT BAYS.

2.8.4.1	WHEN INSTALLED AT 10’ INSIDE DIMENSION SWING ARM SLIDERS WILL TOUCH IN 	CENTER ASSURING GREATEST POSSIBLE WHEELBASE VARIETY FOR LIFT.

2.8.5	WIDTH BETWEEN LIFTING ARMS 8’10” MINIMUM; WIDTH CAN BE WIDENED TO ACCOMMODATE WIDER VEHICLES OR NARROWED FOR TIGHT BAYS.

2.8.6	PAD HEIGHT 3-1/2” AT LOWEST POSITION WHEN THE LIFT IS FULLY LOWERED.

2.8.7	LIFTING HEIGHT 75-1/2” AT THE TOP OF THE PAD AT FULL LIFTING HEIGHT.

2.8.8	LIFTING HEIGHT WITH 3” TRUCK ADAPTORS 78-1/2” AT FULL LIFTING HEIGHT.

2.8.9	LIFTING HEIGHT WITH 6” TRUCK ADAPTORS 81-1/2” AT FULL LIFTING HEIGHT.

2.8.10	LIFTING HEIGHT WITH 3” AND 6” ADAPTORS STACKED TO 9” IS 84-1/2” AT FULL LIFTING HEIGHT.

3.0   HYDRAULICS

3.1	THE LIFT SHALL INCORPORATE A MASTER / SLAVE HYDRAULIC SYSTEM WHICH 	SYNCHRONIZES ELEVATIONS DURING BOTH RAISING AND LOWERING 	OPERATIONS WITH THE MOST ADVERSE RATED LOAD PLACED ON THE LIFT. THE 	LIFT SHALL COME EQUIPPED WITH A FULLY AUTOMATIC LEVELING CONTROL 	AND MANUAL OVER-RIDE AS A BACK UP. CHAIN OR CABLE EQUALIZED LIFTS 	ARE NOT ACCEPTABLE.

3.2	INTERNAL HYDRAULIC SAFETIES ON BOTH CYLINDERS SHALL DETECT MAINSIDE 	OR OFFSIDE PRESSURE DIFFERENTIALS OF LESS THAN 200 LBS. SHOULD THE 	LIFTS 	PRESSURE CHANGE OR AN IMBALANCE CONDITION OCCUR FOR ANY 	REASON, THE LIFT WILL HYDRAULICALLY LOCK ON BOTH SIDES.

3.3	HYDRAULIC CYLINDERS WILL BE MADE OF 2-5/8” CHROME ROD. THE OVERSIZED 	CHROME ROD WILL BE PACKED IN A 4” OD X 3’ LONG BARREL, MINIMUM.

3.4	FULL LOAD WORKING PRESSURE WILL BE A MAXIMUM OF 2,300 PSI. HIGHER 	PRESSURE SYSTEMS WILL NOT BE ACCEPTED DUE TO HIGHER PRESSURES 	CAUSING SEAL LEAKAGE, PREMATURE POWER UNIT FAILURE AND CYLINDER 	WEAR.

3.5	CYLINDER PACKING CONSISTS OF THE FOLLOWING PARKER BRAND SEALS:

DYNAMIC PISTON T - SEALS

2 BACK UP RINGS

2 STATIC O-RINGS

ROD WIPER

ROD T - SEALS

3.6	LIFT WILL BE EQUIPPED WITH EXTERNAL HYDRAULIC SAFETIES CONSISTING OF 	VELOCITY FUSES MOUNTED ON EACH CYLINDER WHICH HYDRAULICALLY LOCK  	IN THE EVENT OF A LEAK, PLUS A FACTORY SET PRESSURE COMPENSATED FLOW 	CONTROL VALVE TO LIMIT DESCENT SPEED.

3.7	SEAMLESS HYDRAULIC STAINLESS STEEL HYDRAULIC TUBING WITH A BURST 	RATING OF 14,000 PSI, MINIMUM. RUBBER, STEEL BRAIDED, OR PLASTIC 	HYDRAULIC HOSES ARE NOT ACCEPTABLE DUE TO SHOP HEAT, WELDING 	SPARKS, AND SLAG CONTACTING RUBBER HOSE, OR FACT THAT RUBBER HOSES 	GET OLD AND BRITTLE WITH USE.

3.8	ALL HYDRAULIC FITTINGS WILL BE STANDARD JIC OR O-RING BOSS FITTINGS. 	SELF FLARING OR COMPRESSION FITTINGS ARE NOT ACCEPTABLE.

3.9	HYDRAULIC FLUID WILL BE DEXRON III, ATF.

4.0   POWER UNIT

4.1	POWER UNIT CAN BE MOUNTED ON EITHER DRIVER SIDE OR PASSENGER SIDE 	COLUMN AND WILL CONSIST OF:

ELECTRIC MOTOR

HYDRAULIC PUMP

STEEL OIL RESERVOIR (PLASTIC RESERVOIRS NOT ACCEPTABLE)

SUCTION STRAINER

HYDRAULIC GEAR PUMP

ALL HYDRAULIC VALVING

4.1.1	ELECTRIC MOTOR IS U.S. MOTORS BRAND 2.0 H.P. 208V / 230V 1 PHASE 60 Hz 	MINIMUM. THE MOTOR WILL HAVE MAXIMUM FULL AMP LOADS 	OF 17.4 AMPS 	@ 208V AND 14.6 AMPS @ 230V.

4.1.2	HYDRAULIC PUMP IS A PRESSURE BALANCED GEAR PUMP WITH FIXED DISPLACEMENT, EXTERNAL TOOTH, AND ALL STEEL GEARS. THE PUMP MUST BE EXTREMELY TOLERANT OF FLUID CONTAMINANTS AND RESISTANT TO GALLING CAUSED BY LOW VISCOSITY START-UP. HARDCOAT PROCESSED INTERNAL PUMP SURFACES FOR EXTENDED SERVICE LIFE.

4.1.3	THE CONTROLS SHALL BE COLUMN MOUNTED WITH THE UNIT OPERATED BY A PUSH UP SWITCH AND A MANUAL DOWN LEVER.

5.0   WARRANTY

5.1 	WARRANTY ON ALL MAJOR STRUCTURAL COMPONENTS (LEGS, CARRIAGES, 	SWING 	ARMS AND SLIDERS) IS A FULL 25 YEARS. MECHANICAL COMPONENTS 	COVERED FOR 10 YEARS.

5.2	HYDRAULIC CYLINDERS ARE COVERED BY AN EXTENDED CYLINDER WARRANTY 	AFTER THE INITIAL 5 YEAR WARRANTY HAS EXPIRED.

6.0   STANDARD EQUIPMENT

6.1	TRUCK ADAPTORS, (4 EACH) OF 3” AND 6” SIZES. THEY MUST BE STACKABLE 	TO MAKE 9” ADAPTERS. FLIP TYPE AND SCREW TYPE PADS ARE NOT 	ACCEPTABLE DUE TO 	LONGER SET UP TIME, HIGHER ARM PAD HEIGHTS OR 	SMALLER LIFT PAD CONTACT SURFACE.

6.2	MALE AND FEMALE ELECTRICAL HUBBELL PLUGS, MALE PLUG PREWIRED ON 	LIFT WITH FEMALE PLUG IN PARTS BOX.

6.3	(16) 3/4” X 5” WEJ-IT ANCHOR BOLTS.

6.4	DEXRON III BRAND ATF FOR HYDRAULIC PUMP AND RESERVOIR.

6.5	SHIMS TO LEVEL THE COLUMNS FOR PROPER INSTALLATION.

6.6 	SAFETY AND OPERATIONS MANUAL.

6.6.1	 ANSI/ALI OIM BOOKLET (ALI STANDARD # ALOIM-2008).

6.6.2	ANSI/ALI LIFTING IT RIGHT BOOKLET (ALI STANDARD # SM01-2).

6.6.3	ANSI/ALI LIFTING POINT GUIDE BOOKLET (ALI STANDARD # ALI/LP-GUIDE).

6.6.4	ANSI/ALI SAFETY DECALS AFFIXED TO LIFT.

7.0   OPTIONAL ACCESSORIES

7.1	WEIGHT GAUGE

7.1.1	THE WEIGHT GAUGE IS A HYDRAULIC “SCALE” ATTACHED TO THE LIFT WHICH SHOWS THE WEIGHT OF THE VEHICLE ON THE LIFT.

7.1.2	THE WEIGHT GAUGE ACCURACY SHALL BE +/- 3% OF FULL SCALE READING.

7.1.3	ALL LIFTS ARE DESIGNED TO BE USED ONCE LOWERED ONTO THE MECHANICAL 	LOCKING DEVICES (REFER TO ANSI STANDARD #SM01-2, “LIFTING IT RIGHT”). THE 	WEIGHT GAUGE SERVES AS A VISUAL CONFIRMATION, AS THE WEIGHT WILL 	SHOW 0 (ZERO) WHEN THE LIFT HAS BEEN LOWERED ONTO THE MECHANICAL 	LOCKS. THE GAUGE WILL ALSO GIVE VISUAL CONFIRMATION TO SHOW IF THE 	LIFT IS OVERLOADED.

7.1.4	WEIGHT GAUGE WILL BE PLACED ON MAINSIDE LIFTING COLUMN AT AN EASY TO 	READ, EYE LEVEL POSITION.	7.1.5	WEIGHT GAUGE OPTION MUST BE ALI 	CERTIFIED TO MEET THE ANSI/ALI ALCTV 2011 AUTOMOTIVE LIFT STANDARD.

7.2	HEIGHT ADJUSTABLE LIFT PAD EXTENDER (SCREW PAD)

7.2.1	A HEIGHT ADJUSTABLE LIFT PAD EXTENDER IS AVAILABLE.

7.2.2	ADJUSTABLE LIFT PAD EXTENDER SHALL BE STACKABLE WITH THE HEIGHT ADAPTERS WHICH ARE NORMALLY SUPPLIED WITH LIFT.

7.2.3	ADJUSTABLE LIFT PAD EXTENDER SHALL RANGE FROM 8 INCHES FULLY RETRACTED AND 11 INCHES WHEN AT FULL EXTENSION.7.2.4 ADJUSTABLE LIFT PAD EXTENDER MUST BE ALI CERTIFIED TO MEET THE ANSI/ALI ALCTV 2011 AUTOMOTIVE LIFT STANDARD.

7.3	SPEEDLANE RAMP OPTION

7.3.1	OPTIONAL SPEEDLANE RAMP OPTION ALLOWS QUICK CONVERSION OF 2-POST LIFT FROM SWING ARM FRAME ENGAGING LIFT TO PAD LIFT OR BACK AGAIN IN LESS THAN 1 MINUTE.

7.3.2	SPEEDLANE WILL ACCOMMODATE MOHAWK’S 9,000 TO 18,000 LB. LIFTS FOR USE IN MULTIPLE BAYS.

7.3.3	SPEEDLANE RAMPS WILL SIT ON TOP OF ARMS USING THE ARMS TO LOCK SPEEDLANE RAMPS IN PLACE.

7.3.4	SPEEDLANE RAMPS WILL BE CONSTRUCTED OF LIGHT-WEIGHT ALUMINUM, PROVIDING EASE OF ASSEMBLY AND REMOVAL TO LIFT OPERATOR.

7.3.5	SPEEDLANE, WHEN ATTACHED TO LIFT, STILL GIVES FULL UNDER-VEHICLE ACCESS FOR ALL REPAIRS.

7.3.6	SPEEDLANE OPTION GIVES TECHNICIAN ABILITY TO NOT SPEND TIME POSITIONING SWING ARMS AT EXACT LIFT POINTS AS IS REQUIRED BY ALL 2-POST LIFTS.

7.3.7	SPEEDLANE OPTION COMES EQUIPPED WITH LOCKS TO HOLD SWING ARMS IN POSITION WHEN AFFIXING SPEEDLANE TO SWING ARMS.

7.3.8	SPEEDLANE OPTION SHALL BE ALI CERTIFIED TO MEET THE ANSI/ALI ALCTV 2011 AUTOMOTIVE LIFT STANDARD.

7.4	FOAM DOOR GUARD OPTION

7.4.1	OPTIONAL FOAM DOOR GUARD OPTION PROTECTS VEHICLE DOORS FROM HITTING THE CARRIAGE AND POTENTIALLY SCRATCHING OR DENTING A VEHICLE DOOR.  DOOR GAURDS ARE MADE OF 2” THICK COATED FOAM TO ABSORB THE IMPACT OF A VEHICLE DOOR.

7.4.2	DOOR GUARDS OF HARD RUBBER OR PLASTIC ARE NOT ACCEPTABLE BECAUSE WHILE THESE HARDER SURFACES WILL PREVENT PAINT SCRATCHES, THEY WILL NOT PREVENT DOORS FROM DENTING IF SLAMMED INTO THE COLUMNS.

7.5	DUAL TROUGH TURF EQUIPMENT OPTION

7.5.1	THE DUAL TROUGH TURF EQUIPMENT OPTION ALLOWS FOR LIFT CONVERSION FROM FRAME ENGAGING CAR AND TRUCK SERVICE TO WHEEL ENGAGING TURF EQUIPMENT MAINTENANCE CAPABILITY (AND BACK AGAIN) IN MINUTES.

7.5.2	THE ALI CERTIFIED DUAL TROUGH TURF EQUIPMENT OPTION FITS BOTH 2 STAGE AND 3 STAGE ARMS.  MINIMUM AND MAXIMUM WHEEL BASE WIDTH VARIES BY LIFT ARM AND MODEL (BELOW):

2 STAGE ARMS (SYSTEM-1A-10 AND TP-18): MIN 49 1⁄ 2” - MAX 109 5 ⁄ 8”

3 STAGE ARMS (LC-12, LMF-12 AND TP-16): MIN 52 1⁄ 2” - MAX 119 1 ⁄ 2”

DUAL TROUGH TURF EQUIPMENT ADAPTER HAS A WEIGHT CAPACITY OF 6,000 LBS. (3,000 LBS./TROUGH).  THESE ADAPTERS ARE RATED ACCORDING TO THE TIRE WIDTH OF VEHICLES (BELOW):

TROUGH CAPACITY:		TIRE CENTER WIDTH:

3000 LBS. 			42” MINIMUM

2500 LBS. 			31” MINIMUM

2000 LBS. 			15” MINIMUM

1500 LBS. 			N/A (NO RESTRICTION)

LIFT MODIFICATION FROM FRAME ENGAGING CAR AND TRUCK SERVICE TO WHEEL ENGAGING TURF EQUIPMENT MAINTENANCE CAPABILITY (OR VICE VERSA) IS LESS THAN FIVE MINUTES.

7.6	WA-1 WHEEL ADAPTORS OPTION

7.6.1 	WHEEL ADAPTORS QUICKLY CONVERT A SWING ARM FRAME ENGAGING LIFT TO BECOME A SWING ARM TIRE ENGAGING LIFT.  WA-1 DO NOT LET SUSPENSION HANG AND OFFER TECHNICIANS A SAFER AND FASTER SET UP OF THE VEHICLE TO BE LIFTED.

7.6.2	WHEN CONVERTING FROM FRAME ENGAGING LIFT TO TIRE ENGAGING LIFT, WA-1 ADAPTORS ARE BOLTED ONTO THE LIFT IN FIVE MINUTES OR LESS OR WHEN CONVERTING FROM WHEEL ENGAGING BACK TO FRAME ENGAGING CAN BE REMOVED FROM THE LIFT IN LESS THAN FIVE MINUTES.

7.7 	UTILITY STATION

7.7.1	OPTIONAL UTILITY STATION AVAILABLE TO MOUNT TO SIDE OF LIFT. UTILITY STATION CONSISTS OF 2/4 GFI 110 VOLT OUTLETS, OIL AND AIR SEPARATOR AND AIR CONNECTION.

8.0   QUALIFICATION OF BIDDERS

8.1	THIS BID WILL BE AWARDED ONLY TO A RESPONSIBLE BIDDER, QUALIFIED TO PROVIDE THE WORK SPECIFIED. THE BIDDER WILL SUBMIT THE FOLLOWING INFORMATION WITH THEIR PROPOSAL.

8.1.1	LIST 3 REFERENCES OF JOBS OF EQUAL VALUE WITH THE SAME SPECIFIED EQUIPMENT.

COMPANY NAME		         CONTACT  			PHONE #

Rev: 2/17

# Text boxes

Certified Accessory

Certified Accessory

Certified Accessory